## Slide 1: ArcGIS On-Line (AGOL)
Lesson #8
Day 2
NAFRI
ArcGIS On Line (AGOL)
Notes: Slide # 1
Lesson #8: ArcGIS On-Line (AGOL)
Lesson Time: 45 minutes (followed by a 15-minute break)
Facilitator Notes:
  Don’t forget to fill in the “Workshop Dates” and “Workshop Location” on the bottom right of this title slide.

## Slide 2: Objectives
Create Fire Danger Rating Areas in ArcGIS Online (AGOL),
Edit FDRAs and/or add Response Areas in Desktop ArcGIS then Synchronize edited data back to AGOL,
Export point fire history data by FDRA.
Notes: Slide # 2
Lesson Objectives:
Demonstrate the ArcGIS Online (AGOL) as a geospatial tool available for developing fire danger rating areas and fire danger plans..

## Slide 3: Video Clip
Notes: Slide # 3
INTRODUCTION:
KEY POINTS:

## Slide 4: Logon to AGOL - Reference Tech Tip 1a
After Acquiring a Logon – id,
Navigate to the FDRA Application.

## Slide 5: Characterize Vegetation, Climate and Topology Reference Tech Tip 1b
Familiarize yourself with the tabs and legends,
Explore the Edit tools,
Review base data best suited for your landscape,
Delineate a polygon for each variable
Vegetation, Climate & Topography.

## Slide 6: Logon to AGOL from Desktop ArcGIS Reference Tech Tip 2a
Work with GIS specialist if necessary,
Using Desktop ArcGIS login to AGOL,
Access the 3 polygons created in AGOL.

## Slide 7: Edit each polygon in ArcGIS Reference Tech Tip 2a
Create a local copy of the 3 polygons for editing and defining the FDRAs,
Edit / move the line location for each polygon to represent the line location of your FDRAs.
Synchronize / copy edits back to the AGOL server.

## Slide 8: Convert Final Break lines into Edge Matched FDRAs Reference Tech Tip 2b
Use the Advanced Editing tool bar,
‘Split’ the 3 characterized polygons into FDRAs,
Attribute each FDRA data table in preparation for Fire History point data clip,
Synchronize polygons back to AGOL.

## Slide 9: If you have Response Areas Reference Tech Tip 2c
Select all Response Areas within your FDRA,
Attribute each Response Area with the FDRA name,
‘Merge’ the Response Areas to your FDRA,
Synchronize data back to AGOL.

## Slide 10: Exporting Fire History by FDRA Reference Tech Tip 2d
The Extraction Tools runs every 5 minutes responding to the attributes in your data table,
After Synchronizing your data back to AGOL Extraction automatically will occur,
Go to web site provided to download your Fire History point data for upload into FF+.

## Slide 11: Conclusion
Working in both AGOL and Desktop ArcGIS,
Delineate your characterized polygons,
Edge match them to you Study Area boundary,
Merge Response Areas if you have them,
Attribute your data to run the Fire History Extraction tool,
Download your Fire History data ready for use in FF+.
Notes: Slide # 11

## Slide 12: Review Objectives
Demonstrate the ArcGIS Desktop and Online (AGOL) as a geospatial tool available for developing fire danger rating areas and export of fire history point data ready for upload into FF+.
Notes: Slide # 12
Review Lesson Objectives:
Demonstrate the ArcGIS Online (AGOL) as a geospatial tool available for developing fire danger rating areas and fire danger plans..

## Slide 13: Questions?
Notes: Slide # 13
Questions?